## Slide 1: 3D Printing of Spherical Harmonic Manipulatives for the Classroom
Josh Grossman Abigail Taylor ‘13

## Slide 2: 3D printing
Types:
  Extrusion
  Binding granular material
  Lamination
  Light polymerization
computer file (STL)
build up material
3D object
a.k.a. additive manufacturing

## Slide 3: 3D printing
Initiated in 1980’s
Research → industry → DIY
Exponential price drop
Recently, rapid progress in capability
  materials, resolution, speed, …
Rapidly expanding market
Used for prototyping and distributed manufacturing
Compare: home/office publishing (2D printing)
  with resources of Internet

## Slide 4: Printer #1: MakerBot Replicator
Extrusion: fused deposition modeling (FDM)
In-house; inexpensive
Thanks to Alan Jamieson,
SMCM Comp Science

## Slide 5: Printer #2: Shapeways service
Bound granular material: selective laser sintering (SLS)
Other materials & methods available
Upload file, make payment, receive objects in mail
Better resolution than MakerBot Replicator
Much higher marginal cost per item, but don’t have to buy printer
Marketplace uploading and purchasing designs
SMCM MakerBot printer broke during project

## Slide 6: Example project: manipulatives of spherical harmonics

## Slide 7: Spherical Harmonics
Angular solutions to Laplace’s equation
Specified by l, m
  l = 0, 1, 2, … and m = -l, …, l
Associated Legendre polynomials
Legendre polynomials

## Slide 8: Spherical Harmonics
Often initially confusing to students
Geometric properties not immediately evident

## Slide 9: Spherical Harmonics

## Slide 10: Process
Equations
Mathematica
STL file
Software converts for printing
Print
Finishing
(optional)
Additional processing
(optional)
e.g. ReplicatorG
for MakerBot
Export["00441.STL",
RegionPlot3D[315*Abs[SphericalHarmonicY[0,0,ArcCos[z/(x^2+y^2+z^2)^(1/2)],ArcTan[y/x]]^2]<(x^2+y^2+z^2)^(1/2)<315*Abs[SphericalHarmonicY[0,0,ArcCos[z/(x^2+y^2+z^2)^(1/2)],ArcTan[y/x]]^2]+1.1,{x,-45,45},{y,-45,45},{z,-45,45},PlotPoints->150]]

## Slide 11: MakerBot models
Honeycomb for solid interiors
Overhangs problematic → print ½’s or ¼’s, then glue
Zero thickness at origin →
Individual plastic strands apparent → sand and paint
~$1 each

## Slide 12: Shapeways models
Add thickness
$15-$45 each

## Slide 13: Uses
Spherical harmonic manipulatives used in Quantum Mechanics class and Atomic Physics study group
Illustrated geometric features
Prompted student discussion

## Slide 14: What’s next?
http://faculty.smcm.edu/jmgrossman/research/ed/3Dprinting.html
diagram from Hyperphysics
Models of other 3D mathematical abstractions
  PvT phase surfaces for Thermodynamics classes, …
Real objects for experiments
  Gears, wheels, moment of inertia test objects, …
What would you do?
By user ngoodger on Thingiverse
Fluid filters by user siderits on Thingiverse